TR-200 Parts Identification Guidelines

Below are a list of common requirements and issues associated with identifying TR-200 drives in the field and at the Parts counter.  This list is meant to assist you in collecting all of the correct information about a drive as early as possible in the ID process.  Doing so might save the technician extra calls or trips to the job site.

- On the Danfoss TR-200 VFDs there are two labels each with a serial #, model # and product / material # on them.

- There is a white label on top or side of the drive which will have the serial # and # for the product / material # identifying the drive. See Figure 1

- There is a white label on the inside of the control / by-pass door which will have an serial # and the product/ material # to identifying the control / by-pass & drive assembly. See Figure 2

- Have the customer / tech provide all, the product / material #, serial # off the VFD panel and drive plus the model #, serial # off the unit in which the VFD is attached to.

- Here is and example what the information will look like.

Product / Material #        Serial #

178B5550                  038726H517

174F9991                   237600Y517

Model # TR16002GT6B20STR0DLF00A00C0

131L1002                 058702H339

174Z4428                 964803Y359

Model # TR-200P4K0T4E20H2XGXXXXSXXXXAXBXCXXXXDX

The last three digits of the serial # will tell us the week and year the unit was built.

Example 517    51 week, year 2007

Example 339	 33 week, year 2009

- Once we know the drive product / material # we can cross it in Pride /Oracle OC for the Trane part #,

  - Example 178B5550 = DRV00296

  - Example 131L1002  =DRV00570

  - Example 130B2799 = MOD01800

- You can take the Trane part # DRV00296 enter it into CATS as a model # for a parts list of the drive only (TR1 drive only). For the control / by-pass components & TR200 drive components you will need to contact Global Parts, Parts ID @ partsid@trane.com

- If the customer / tech can provide us where the part is located or with a wire designator within the drive or control / by-pass it will be very helpful in identifying the correct part.  Example 1K40 = M3 bypass contactor or 1K41= M1 or M2 drive contactor U1, K42, K43= overload -  See Figure 3

- Any other Danfoss drives other than TR-200 drives, example (VLT6000, VLT5000, VLT8000, VLT2800, etc) needs to be serviced by Danfoss---at least part need to be identified directly from Danfoss.

Example:

VLT6022GT4CN1STR0DLF00A00C0----This is a VLT6000

TR16002GT6B20STR0DLF00A00C0--This is a Trane drive TR16000

VLT5022PT2C20STR0D0F00A00C0--this is a VLT5000

The beginning letters may change if it is a drive and bypass are engineered-to-order but the 4 digits following will tell you what series.

- If, assistance is needed contact; Global Parts, Parts Identification Group partsid@trane.com

Great publications to look at are or just type TR200 in the Keyword block in E-Library for more additional information:

BAS-PRC034-EN		PART-SVB21A-EN		PART-SVN116A-EN

BAS-SLB26-EN		PART-SVB22B-EN		PART-SVN117A-EN

BAS-SVP048-EN		PART-SVB24A-EN		PART-SVN121A-EN

BAS-SVX19B-EN		PART-SVB25A-EN

BAS-SVX21A-EN		PART-SVB26A-EN

BAS-SVX22A-EN

Important note is:

Panels / CNTs will have an 174# Drives will have a 131L# Parts will have a 130B# or 176U#  for TR200 drives.

Figure1

Figure 2

Figure 3